## Slide 1: Superfast Parasitic Extraction for Frequency Domain EM-Circuit Simulation
IMS200Adviso3/RFIC2003
Dipanjan Gope
Notes: This is a sample presentation template

## Slide 2: Outline
Parasitic Extraction in Cutting-edge Circuit Design
Existing Fast Algorithms
Superfast Parasitic Extraction
Comparative Study with Existing Algorithms
Application to Practical Layouts
Conclusions and Future Work
Notes: This is the flow

## Slide 3: Parasitic Extraction
Deep Sub-micron technology
- High aspect ratio to reduce wire resistance
- Minimum wire spacing
- Wire delay exceeds gate delay
High Frequency Applications
- Delay analysis critical
- Delay computed from parasitic models
Increase in
parasitic
capacitance
Extraction
of parasitics
imperative
SIA97: SRC’s 10 year report
Minimum Feature size | 250nm | 70nm
Min Spacing | 340nm | 100nm
Aspect Ratio | 1.8:1 | 2.7:1
Gate Delay | 0.075ns | 0.029ns
2cm Wire Delay | 2.12 ns | 3.53ns

## Slide 4: Fast Extraction Algorithms
Numerical Methods required
- 3D complex on-chip/package/board geometries
- High accuracy solutions
Integral Equation based Solvers: e.g. Method of Moments (MoM)
- Smaller sized system
- Well conditioned system
- Dense system of equations
Solver Type | Memory | Time
Direct | 20GB | 10 months
Iterative | 20GB | 14hrs
Fast Iterative | 10MB | 10min
Fast Solvers for Method of Moments: O(N)-O(NlogN) memory and time
- Fast Multipole Method
- Pre-corrected FFT Method
- QR based Method

## Slide 5: IES3: QR based Fast Solver
QR decomposition of a far-interaction
n sources
m observers
=
geometry
matrix
Geometry recursively subdivided to form a binary tree
- 3d box divided along its largest coordinate
- Resultant boxes of unequal shapes, sizes and separation
Rank-Map oriented matrix formation
- Rank-map provides the starting point of matrix formation
- Fine tuned by merges/splits
Typical Matrix Structure

## Slide 6: Algorithm flow of IES3

## Slide 7: Merits and Demerits of IES3
Kernel Independent Method
- Directly applicable to multi-layered medium
Low Frequency Stability
- Unlike FMM applicable to small electrical structures
Less Memory and Number of Matrix Vector product operations
- Even for free-space capacitance extraction problems
High Setup Time
- Ideal Rank-map impossible to construct
- Conservative Rank-map will necessitate more merges
- Liberal Rank-map will waste time doing unacceptable QRs
- Bad choice for large problems with interest in limited number of nets

## Slide 8: DICOT-QR: Superfast Iterative solver
Deterministic Interaction Capacitated Oct-Tree Based QR
A smart mix of the best of both algorithms
- QR decomposition of low-rank interaction matrices : IES3
- Oct-Tree based regular geometry of levels of cubes : FMM
2. Optimum compression through merged interaction list
- FMM interaction shells merged FMM shells and QR flexibility
Maintain the compression of IES3 with faster setup
- Accurate matrix structure pre-determined by Merged Interaction List
- Deterministic matrix structure precludes merges and unwanted QR

## Slide 9: Geometry and shell structure of FMM
Oct-Tree decomposition in 3D
- Each cube is broken into equal sized 8 children cubes
Geometry recursively decomposed into levels
FMM interaction shell for each cube
- Similar shell for all cubes across levels

## Slide 10: Merged Interaction List
Siblings have common cubes in their interaction list
Merging sibling observers and common cube sources
- Based on maximum memory compression
- Identifying merged interaction list for 1 sibling combination
- Same pattern repeats for all sibling combinations and across levels
- Merged interaction list replaces “rank-map” of IES3
- Merged interaction list possible due to regular geometry
One entry of Merged Interaction List

## Slide 11: Merged Interaction Lists

## Slide 12: Time and Memory Scaling
Simple 5 X 5 bus
Issues | FastCap | DICOT | RMBT
Memory | 3GB | 1.9GB | 2.2GB
Time | 187min | 122min | 170min
Max size | 0.4million | 0.7million | 0.6million
memory
time
*
* At 0.4 million unknowns
SAME ACCURACY IN SOLUTION
ALGO | SETUP | GMRES
QR | 1e-3 | 1e-3
FMM | P=2 | 1e-3

## Slide 13: Time Scaling with number of RHS
101,600 patches 14 lead structure
Memory
- Fast-Cap 678MB
- RMBT-QR 445MB
- DICOT-QR 441MB

## Slide 14: DARPA Test Example (ic_hrl_tc1)
0.1 million patches
6 RHS solutions

## Slide 15: Performance Comparison
Algorithm | Memory | Time
DICOT-QR | 365MB | 19min
RMBT-QR | 380MB | 27min
FAST-CAP | 500MB | 30min

## Slide 16: Capability of Superfast DICOT-QR
30 copies of ic_hrl_tc1 placed in 10 X 3 array
0.9 million patches; 1200 nets
QR Tolerance 1e-3; GMRES Tolerance 1e-3
Algorithm | Memory | Setup | Solve (3RHS)
DICOT-QR | 3.3GB | 48min | 90min
RMBT-QR | Could Not Fit in Memory |  | 
FASTCAP | Could Not Fit in Memory |  | 

## Slide 17: Conclusions and Future Work
Superfast QR Iterative solver based on “best of both algorithms”
- Memory optimized as in IES3
- Solve time optimized as in IES3
- Setup time drastically reduced from that of IES3 using FMM features
Versatile applications
- Parasitic capacitance extraction (electro-static): presented
- Parasitic inductance extraction (magneto-static)
- Layered medium
- Electric field integral equations coupled to circuits
- Magnetic field integral equations coupled to circuits
- PMCHW coupled to circuits
- Time domain QR fast solvers