## Slide 1: BMAC: Behavioral Model Analyzer and Compiler for Circuit Simulation of Mixed-Technology Systems
IMS2003/RFIC2003
BMAC Group
MSCAD Lab
University of Washington
Notes: This is a sample presentation template

## Slide 2: Group Member
Bo Wan
Bo Hu
Lili Zhou

## Slide 3: Outline
Current state of compact device model implementation
Model compiler definition
Modified device model implementation flow
Mixed-Technology co-simulation
Results
Conclusion
Milestones
Notes: This is the flow

## Slide 4: Typical Model Flow

## Slide 5: Model Developer Issues
Model implementation is more difficult than model creation
Software implementation is time consuming and error-prone
Requires independent implementations for different simulator vendor
Requires close cooperation with the vendor
A lot of new model created, few implemented
Modification of model is difficult

## Slide 6: Designer Issues
Want accurate and robust models
Want a wide range of models to be available and easily obtainable
Want all models to simulate efficiently
Want to easily modify the device equations to add new effects

## Slide 7: Model Compiler Definition
A Model Compiler is a CAD tool that supports fast implementation of compact device model.
Model Compiler
BMAC
Input
Output
Input: compact device models described in high level language VHDL-AMS
Output: device code in C/C++ that can be directly compiled in Cosmos/spice.

## Slide 8: Typical Implementation Flow for New Device Model
Convert to C code
New device &Equations
Initial coding in MATLAB
Purchased by design company & Qualification
Release new simulator
Designers using new model
Install & test of the model in simulator
New modification
New effect update

## Slide 9: Reduced Implementation Flow Using MCAST
New device Equations or Initial MATLAB codes
Automation tools (Paragon etc)
VHDL-AMS codes
Integration into public or commercial simulator
Designers using new model
BMAC
New modification
New effect update

## Slide 10: Model Compiler Processing Flow

## Slide 11: Architecture of BMAC

## Slide 12: Modified Model Flow

## Slide 13: Block diagram in VHDL-AMS

## Slide 14: BSIMSOI model in VHDL-AMS
module soimos(drain, gate, source, ebulk);
inout drain, gate, source, ebulk;
electrical drain, gate, source, ebulk;
electrical pbody,body;
`define SMOOTHFACTOR 0.1
`define EPSOX 3.453133e-11
`define EPSSI 1.03594e-10
……………..
parameter integer mB3SOItype = `NMOS;
parameter integer mB3SOImobMod = 1;
parameter real mB3SOIa0 = 1.0;
parameter real mB3SOIags = 0.0;
……………..
//////////////////////////////////EQUATIONS///////////////////////////////////////
analog
begin
@(initial_step or initial_step("static"))
begin
Cboxt = mB3SOIcbox * mB3SOIcsi / (mB3SOIcbox + mB3SOIcsi);
………………
vds = mB3SOItype * V(drain, source);
……………….
I(drain) <+ mB3SOItype*(Ids + Ic - Ibd + Iii + Idgidl) + mB3SOItype*ddt(qdrn);

## Slide 15: Mixed-Technology Issues
Rising demand for concurrent mixed-technology co-design
Heterogeneous effects need to be considered: electrical, electromagnetic (RF and microwave), thermal, optical, chemical, mechanical, etc.
Currently no CAD tool that support the concurrent modeling and simulation of mixed-technology devices

## Slide 16: Mixed-Technology Simulation Methodology

## Slide 17: Example: A Thermal resistor
….
entity wbr is
generic ( r2 : real := 1.0e3; alpha : real := 0.1 );
port ( terminal pos, neg : electrical; terminal t1, t2 : thermal );
end wbr;
architecture arch1 of wbr is
quantity volt across curr through pos to neg;
quantity temp across heatflow through t1 to t2;
begin
Thermal_equations: procedural is
begin -- procedural statements
curr := volt / (r2 + alpha * (temp - tref) );
heatflow := -volt * curr;
end procedural;
end architecture arch1;

## Slide 18: Thermal resistor test circuit
Parameters used:
    V1 : step Pulse, 1v
    V2 : 1v
    R1=R2=R3=R4=1k ohm
    Rt1=Rt2=Rt3=1000K

## Slide 19: Result: Voltage over R2 and R3

## Slide 20: Example: Laser diode model
…
ENTITY LD IS
GENERIC (T:REAL)
PORT(TERMINAL P, M: ELECTRICAL;
TERMINAL J: RADIANT);
END LD;
ARCHITECTURE BEHAVE OF LD IS
…
QUANTITY V ACROSS I THROUGH P TO M;
QUANTITY OPTIC_POWER ACROSS OPTIC_FLUX THROUGH J TO RADIANT_REF;
QUANTITY Z: REAL;
BEGIN
NE*EXP(Q*V/(N*K*T))*(Q/(N*K*T))*V'DOT == I/(Q*VO)-(NE/TAUN)*EXP(Q*V/(N*K*T))+NE/TAUN-
GO *EXP(-T/TOA)*(NE*EXP(Q*V/(N*K*T))-NO *EXP(T/TOA))*(1.0-EPEPSILON*THITA*(Z+SIGMA)*(Z+SIGMA))
*THITA*(Z+SIGMA) *(Z+SIGMA);
2.0*Z'DOT == GAMMA*GO *EXP(-T/TOA)*(NE*EXP(Q*V/(N*K*T))-NO *EXP(T/TOA))*(1.0-EPSILON*THITA
*(Z+SIGMA)*(Z+SIGMA)) *(Z+SIGMA)+(GAMMA*BETA*NE)/(THITA*TAUN*(Z+SIGMA)) *EXP(Q*V/(N*K*T))-
(Z+SIGMA)/TAUP;
OPTIC_POWER==(Z+SIGMA)*(Z+SIGMA);
END BEHAVE;

## Slide 21: Result : Laser Diode

## Slide 22: Results
Device Models Implemented by MCAST
Device Model
# Nodes
# Parameters
Complexity
(#line of VHDL-AMS code)
MOS Level 1
4
2
40
MOS Level 3
4
121
870
BSIM3
4
412
2228
BSIMSOI
6
787
6660
EKV
4
40
116

## Slide 23: Results
Table 2. Benchmark Circuits
Circuit
# Transistor
One-shot
22
VCO
10
Power AMP
4
Ring Oscillator
12
Comparator
38
INV
2
NAND
4
NOR
4
AOI22
16
OAI22
16
Adder
55
Complex Cell
50
INV chain
8
12-bit Adder
660

## Slide 24: Accuracy
Boeing Comparator

## Slide 25: Accuracy
VCO

## Slide 26: Accuracy
One-shot Plus Generator

## Slide 27: Accuracy
Power Amplifier

## Slide 28: Accuracy
Ring Oscillator

## Slide 29: Efficiency

## Slide 30: Efficiency
Scalable
100x-1000x
speed up!!!

## Slide 31: Conclusions
MCAST is the first model compiler that can handle industry-grade device models, such as BSIM3 and BSIMSOI
Generated model is very accurate
Generated model is very efficient
MCAST supports devices in multi-physics domain
(MCAST + COSMOS/SPICE) supports Mixed-Technology co-simulation

## Slide 32: Milestones
Aug. 2002: MCAST supports BSIM3
Dec. 2002: MCAST with optimizations
Mar. 2003: MCAST with BSIMSOI, EKV etc.
Jun. 2003: MCAST release, Demo & Test in Boeing
June 2003: MCAST supports Mixed-Technology simulation
Sep 2003: MCAST release with Frequency-domain/Behavioral modeling
Dec. 2003: MCAST release with digital modeling
Jun. 2004: Final release of MCAST

## Slide 33
Thank you!