## Slide 1: Progress on Linear Solvers
Research Team Members:
Dr. Guoyong Shi
Zhao Li, Bo Hu
Mixed Signal CAD Research Lab
Department of Electrical Engineering
University of Washington, Seattle WA

## Slide 2: CoSMoS Linear Solver Candidates
  SPARSE1.3 (Direct solver in SPICE)
  SuperLU (Direct solver)
  AZTEC (Direct and iterative solver)
  HYPRE (Direct and iterative solver)
  DASSL (DAE solver)

## Slide 3: Goals
Multiple solver options for different circuit simulation problems
Unified circuit-EM formulation
Orders of magnitude speed-up

## Slide 4: Achievements
All solver libraries have been installed in our Unix box
Evaluations have been made on direct solvers: SPARSE1.3 and SuperLU
  SuperLU can be an alternative for circuit simulator (SPICE), i.e., DC analysis
Distributed parallel solvers (AZTEC, HYPRE) are options for EM coupled simulation
  HYPRE is the option for stamping EM components
DASSL is the option for direct simulation without discretized stamping (speed-up for some circuits)

## Slide 5: Conclusions
Direct solvers
  SuperLU is good for well ordered matrices
  SPARSE1.3 is good for repeated solving of the same patterned matrix
Solvers for distributed problems (i.e., EM)
  Stamping based formulation – HYPRE is a good option

## Slide 6: Targets
Ordering is the key to speedup direct solvers
  Multiple solver options
Stamping based matrix building unifies circuit and EM formulation
  Stencil used in HYPRE is stamping for distributed components
Stamping based matrix formulation can unify ODE and PDE simulation
Mixed solvers are needed for unified formulation

## Slide 7: SILCA Semi-Implicit Linear Centric Analysis
PhD Student: Zhao Li
Advisor: Richard Shi
Mixed Signal CAD Research Lab
Department of Electrical Engineering
University of Washington, Seattle WA

## Slide 8: Challenges for Time-Domain Circuit Simulation
Accurate analysis of VLSI circuits together with surrounding environments
  Power/ground network, common substrate, interconnect lines, packaging inductance, etc.
  Deep-submicron circuits with extracted parasitic effects
  Coupled circuit-EM simulation
  Thermal analysis

## Slide 9: Per-iteration Cost Distribution in Transient Simulation
Device evaluation
  Table look-up models
  Parallel and distributed computation
LU factorization
  Sparse matrix solvers O(n1.1~1.5)
  Close to worst case O(n3) considering surrounding environments
Forward/backward substitution(FBS)
  Much lower than LU factorization
Decrease LU cost !

## Slide 10: Proposed Linear Centric Circuit Analysis Methods
Improve numerical integration formulae to keep circuit matrices constant for a large time interval
  Semi-implicit integration formulae as a predictor
  Iterative integration formulae as a corrector
Improve nonlinear iteration methods to keep circuit matrices constant for a large voltage range
  Successive variable chord method
  Rank-one update technique

## Slide 11: Semi-Implicit Trapezoid (SI-TRAP) Formula
Variable-step integration formula – h is the basis time step size,  is the variable-step factor
Constant conductance

## Slide 12: Numerical Stability of SI-TRAP
= 0.5
= 2
SI-TRAP is only A-stable when  < 1, so it is only used as a predictor when  < 1

## Slide 13: Iterative Trapezoid (IR-TRAP) Formula
Constant conductance
LTE is the same as TRAP if converge successfully

## Slide 14: Numerical Stability of IR-TRAP
= 0.625
k = 2
= 2.5
k = 2
Absolute stability region is related to k

## Slide 15: Numerical Stability of IR-TRAP
= 0.625
k = 10
= 2.5
k = 10
Absolute stability region approaches to that of standard TRAP method with k

## Slide 16: Linear Circuit Analysis Example
Two RCL circuits with 100X time constant difference
Initial time step size 0.01 sec, simulation interval 160 sec, 16001 simulation points for fixed time-step methods

## Slide 17: Time Step Size Distribution
Less than 3000 simulation points
Most time step sizes between 0.05 and 0.2 sec

## Slide 18: Basis Time Step Size Distribution
Constant basis time step size means constant equivalent conductance

## Slide 19: Applications of Successive Chord Iteration
Weakly nonlinear analysis for Analog/RF circuits
  Implemented in harmonic balance analysis (CMU)
Timing analysis of single-stage logic gate driving interconnect lines
  TETA (CMU)
Main drawback – A chord ensuring convergence generally leads to a slow convergence rate

## Slide 20: Piecewise Weakly Nonlinear Analysis (PWNL)
Different local chords are defined for different weakly nonlinear segments – Successive Varaible Chord (SVC)

## Slide 21: Successive Variable Chord Method for MOSFET
 | gm | gmbs | gds
Reg#0 | 0 | 0 | 0
Reg#1 | 0 | 0 | gds-1
Reg#2 | 0 | 0 | gds-2
Reg#3 | gm-max | gmbs-max | gds-3
Reg#4 | gm-max | gmbs-max | gds-4

## Slide 22: Rank-one Update
A local chord update will only affect four elements in the circuit matrix
  Is a new LU factorization necessary?
Householder ‘s formula
Update of L\U matrices – O(m*n2)
  Toshio Fujisawa, et. al., “A Sparse Matrix Method for Analysis of Piecewise-Linear Resistive Networks”, IEEE Trans on Circuit Theory, vol. CT-19, no. 6, pp. 571-584, Nov. 1972

## Slide 23: Substrate Coupling Example

## Slide 24: Feed-through via Substrate

## Slide 25: Speed-up vs. #Elements

## Slide 26: Power/Ground Example

## Slide 27: IR-drop and L*dI/dt effects

## Slide 28: Test Summary
Over 80X LU speed-up and 20X overall speed-up on substrate and power/ground examples
More speed-up for larger systems
Speed-up reasons
  High LU/FBS cost ratio – large & dense systems
  High LU speed-up – RCL parasitic effects
  Rank-one update for fast LU factorization
Test a few digital and analog circuits

## Slide 29: Conclusions
SILCA – A prototype of time-domain nonlinear circuit simulator
  Variable-step semi-implicit iterative numerical integration formulae
  PWNL analysis realized by the SVC method
  Rank-one update technique
  Orders of magnitude speed-up
  Work without derivatives if required

## Slide 30: Schedule
Summer Quarter (June  Sept, 2003)
  More research on PWNL analysis
  Compare with DASSL (fixed leading coefficient BDF)
  More test examples
Next 6 months ( Dec 2003)
  Decoupled nonlinear/linear circuit simulation
  Integration of nonlinear capacitors