## Slide 1: Fast Frequency Domain Simulation of Coupled Systems
Todd West
Notes: This is a sample presentation template

## Slide 2: Agenda
Changes in AFSA
  Advanced Field Solver Architecture
  progress in last six months
Research Directions
  current status
  early FMM results
  plans for next six months

## Slide 3: Advanced Field Solver Architecture
multiphysics simulation engine
  currently operates in frequency domain
  supports circuits and electromagnetics
fully modular
  easy to add new electromagnetic formulations
  extensible to time domain, thermals, other physics
targets workstation simulation
  “limited” computing resources
  focused on fast solvers

## Slide 4: December 2002 POR – Frequency Domain Module
geometry library
quadrature library
field solver library
controller/user interface
(Matlab test driver)
coupled EM codebase
CoSMoS solvers
Spice/HDL manager
(circuit test driver)
CoSMoS infrastructure
EM and EM to circuit coupling matrices

## Slide 5: Current POR – Standalone Frequency Domain Simulator
geometry
quadrature
EM field solver
developer interface
circuit system
coupled system
Matlab
user interface
Windows GUI
BLAS, LAPACK
SuperLU
hybrid solver

## Slide 6: Architectural Improvements
<source|Green’s function|test>
  flexible quadrature extensible to equivalence principle EFIE, PMCHW
upgrades of entire object hierarchy
  architecture is stable
code unified into a single language
  26,500 lines of C++
API refinements and improved robustness
  approaching beta status

## Slide 7: New Features
multilevel adaptive fast multipole algorithm
  quasistatic EFIE
  several preconditioners implemented
  scalable to full wave, equivalence principle EFIE, PMCHW, electrostatics, and magnetostatics
hybrid solver
  EM dense LU solution, circuit sparse LU solution
  EM iterative solution, circuit sparse LU solution
vastly improved documentation
  API, configuration files, and physics formulations

## Slide 8: Research Status
fundamental infrastructure in place
  ready for true coupled system simulation
  gathering test suite of analog RF designs
basic analysis of FMM performance done
  works with on-die systems!
  data structures and algorithms tuned
  preconditioners surveyed (need faster ones)
hybrid solver for coupled systems
  starting preconditioner survey for hybrid FMM

## Slide 9: Multilevel Adaptive Fast Multipole Algorithm (MLAFMA)
O(Nlog(N)) method for fast solution
  clustering derived from electromagnetic physics
  adapts clustering to mesh and system resources
  FMMs best understood class of EM fast solver

## Slide 10: MLAFMA for a DARPA test case NCSU 0.25m spiral pair
geometry makes fast solution challenging
  degrades FMM efficiency
  causes other FMM codes to resort to “cheating”
  but LU normally faster for N2000–4000

## Slide 11: Research Directions
simulate current analog RF designs
  establish baseline on EM and circuit use
increase FMM performance
  goal is fast convergence of circuit coupled FMM
  electrodynamic preconditioning not well known
  preconditioning of coupled systems unexplored
  also continue tuning implementation
fast approximate solution
  FMM accelerated Padé expansion

## Slide 12: Parting Shot
hybrid FMM solution of NCSU spirals

## Slide 13: Backup Hybrid Solvers
different physics: different solvers
  want to use best available solver for each part of system
  fast iterative solver for EM
  sparse LU for circuit system

## Slide 14: Backup Reduced Systems
connection models
  compressed form of system matrix
  fast exploration of variations in circuit or EM parts
reduced order models
  fast solution of entire system