## Slide 1
ODT
Tom Friddell
Associate Technical Fellow, Microelectronic Design
Boeing Electronic Systems
Seattle, WA
Phone: (253) 773-9277
Presented to DARPA
June 19, 2003
Boeing CoSMoS Tool Evaluation

## Slide 2: Outline
Introduction
Description of the Evaluation
Tools Evaluated
Results
Remaining work

## Slide 3: Introduction
Boeing is in a unique position to evaluate EDA infrastructure
  Actively using a state-of-the-art military ASIC development flow
  Related program involvement – e.g. ACME, DTRA-RHM, VDSM
  Not foundry-captive: Foundry-flexible design flow
  Not EDA vendor-captive
  Capability ranges from front-end to back-end and test, RF, Analog, Digital, and mixed-signal design
  Technology background: Sub-micron, SiGe, SOI, Bipolar, CMOS…
Boeing Role on CoSMoS
  Contribute test cases, user feedback, and design expertise
  Evaluate tool capabilities
  Provide EDA deployment test bench

## Slide 4: Related Tool Experience
Application of Orora Tools to Avoid a Design Problem

## Slide 5: Related Tool Experience (Cont’d) The BoeSTM Problem
8b 40 MHz Pipelined ADC
New design did not function on first pass
Difficult to diagnose
Repeatability issues
Required experience
Design, test, or process?
Cause: Routing via mismatch

## Slide 6: Related Tool Experience (Cont’d) If Arana/Arsyn had Been Used
In the test diagnosis stage:
  Shorter analysis/test time – parasitic effect analysis
  Quicker to find a solution
In the design review stage:
  The mis-matching problem was spotted by the very experienced designers, however, thought to be OK (only 1 or 2 ohms)
  Tools could have avoided a second pass
Best in the design stage:
  Sensitivity analysis helps designers spot critical design points
  Arsyn helps obtain more robust design – larger design space explored, what if analysis, automated search

## Slide 7: Related Tool Experience (Cont’d) Impact of Arana/Arsyn
Successful test use by Boeing SSED
Cut design time in half
Reduce expertise needed for success
Eliminate expensive debugging and additional pass
Arana/Arsyn has become a key part of the Boeing mixed-signal design flow

## Slide 8: Introduction: Boeing Task Overview
Establish Evaluation Criteria
User Requirements
Prepare Design Development Data
CoSMoS Evaluation
Host CoSMoS at Boeing
CoSMoS Benchmarking
Final Report
FROSTY, IPRAIL, BMAC
Now
Remaining CoSMoS Functionality & Final Versions

## Slide 9: Description of the Evaluation
Evaluated three tools from the CoSMoS toolset: BMAC, Frosty, and IPRAIL
Evaluation Criteria:
  Engineering time savings
  Suitability for production engineering design flow
  Ease of use and skill requirements
  Potential for reducing engineering errors
Evaluation team: 5 Digital/Analog/RF/EDA Boeing engineers
Evaluation included
  UW presentation and tool demonstration
  Installation from scratch on a clean system

## Slide 10: FROSTY
Function
  Extract high-level netlist from layout database
Strengths
  Simulation of gate-level behavioral model much faster than transistor-level simulation
  Flexible, process-independent input files
Applicability
  Layout verification by simulation
Applications: Verification, DMS Part Reverse Engineering
Fast Hierarchy Extraction Tool

## Slide 11: IPRAIL
Function
  Analog library retargeting
Strengths
  Preserves expert knowledge from existing layout by feature recognition, e.g. symmetry
  Scales and compacts layout to new technology rules
Applicability
  Allows reuse of handcrafted analog layouts in new process
Applications: Library port between compatible processes
Layout
Technology Files,
Sizing
Fully-Routed Re-Sized Layout
IPRAIL
Intellectual Property Reuse Analog IC Layout

## Slide 12: BMAC
Function
  Auto-generate simulator model code from high-level language
Strengths
  Allows expression of device behavior in high-level language
  Saves much time generating all files necessary for simulator integration
  Virtually eliminates debug time as code is generated correctly
Applications: Foundry process setup, modeling acceleration
BMAC
VHDL-AMS Model
SPICE Model
Behavioral Modeling Analyzer Compiler

## Slide 13: Evaluation Results
Productivity
Productivity Improvement – All tools are capable of reducing engineering flow time for their function. IPRAIL can greatly reduce library port time between compatible processes – may require adjustments for new parasitics.
Production Readiness – Some user documentation and initial setup effort remains. File structure changes needed for integration into production environment.
Skill Level – No difficult skill requirements.
Potential for reducing engineering errors – FROSTY could augment existing design verification, IPRAIL eliminates manual layout work in porting libraries.
Production Readiness
Skill Level
Error Reduction
5 – 10x
FROSTY
Near
Medium
High
2x
IPRAIL
Near
Medium
Good
2x
BMAC
Near
Low
Good

## Slide 14: Evaluation Comments
All tools performed their function – Actual hands-on work needed for a final evaluation
Pre-release versions evaluated represent an initial capability with growth potential, e.g. number of circuits recognized by Frosty
Some tools would benefit from integration with a design database system like Milkyway or DFII.

## Slide 15: Remaining Tasks
Provide continuing design center support to develop additional CoSMoS functionality as it becomes available
Installation of CoSMoS tool set at Boeing 4Q03
Hands-on benchmark CoSMoS tools against existing and other automated design tools to quantify design time and error reduction 1Q04
Final report 2Q04