## Slide 1: Working Towards the Peaceful Coexistence of Wireless PANs, LANs, and WANs Northcon 2002 Tutorial
Rob Roy
Sr. Director, Business Development & Tech Strategy
Mobilian Corporation
rob.roy@mobilian.com

## Slide 2: Agenda (1)
Introductions
Overview of 802.11, 802.15, and 802.16
  Includes all current Task Groups and Study Groups
Current Status
Coexistence: The Unlicensed band problem
Mixed 802.11b/a/g environments
Emerging trends
  Higher speeds
  More features
  New technologies, such as smart antennas
What about Ultra Wide Band (UWB)?

## Slide 3: Agenda (2)
The convergence of 802.11, 15, 16, and 3G/4G mobile
  Roaming from WLAN to WWAN
The multi-standard, multi-band radio – is it the answer?
A case study: The WPAN/WLAN combo radio
Conclusion

## Slide 4: Introduction: About Mobilian….
Fabless semiconductor company
Focus: TrueConnectivity
  Multi-standard, integrated radio technology
  Coexistence technology
Our view of the wireless future…
  Multiple standards (PAN/LAN/WAN) will always exist
    Each is optimized for a different environment
  Integrated solutions and combinations of standards will improve seamless connectivity (“It just works”) and become the norm

## Slide 5: Overview of WPAN/WLAN/WWAN
WPAN – 802.15
WLAN – 802.11
WWAN – 802.16
And how this fits with 3G/4G

## Slide 6: Wireless PAN
Definition of a WPAN:
  “The 802.15 WPAN™ effort focuses on the development of consensus standards for Personal Area Networks or short distance wireless networks. These WPANs address wireless networking of portable and mobile computing devices such as PCs, Personal Digital Assistants (PDAs), peripherals, cell phones, pagers, and consumer electronics; allowing these devices to communicate and interoperate with one another. The goal is to publish standards, recommended practices, or guides that have broad market applicability and deal effectively with the issues of coexistence and interoperability with other wired and wireless networking solutions”
Short range cable replacement: typically <10m

## Slide 7: The WPAN world….
IEEE 802.15 has 4 Task groups:
  802.15.1: The Original WPAN – aka Bluetooth
    The Bluetooth protocol in an IEEE package, with PHY/MAC definitions
    2.4 – 2.4835 GHz ISM band
  802.15.2: Coexistence Task Group
    Developing a “Recommended Practice” for coexistence between 802.15.1 and 802.11b
  802.15.3: High rate WPAN
    Designed for consumer multimedia applications, up to 55Mb/s data rate with Quality of Service (QoS)
    802.15.3a (SG): investigating alternative (UWB) physical layer
  802.15.4: Low cost, low power wireless for devices such as sensors, toys

## Slide 8: Wireless LAN
Definition of a WLAN:
  A wireless version of a local area networking protocol such as Ethernet. Since a WLAN interoperates with a wired LAN, its behavior must be compatible with other portions of the LAN infrastructure, such as TCP/IP.
WLAN must act like Ethernet over an unreliable medium
  Uses CSMA/CA with backoff
  Uses beacons to maintain synchronization
  Uses CTS/RTS for “hidden nodes”

## Slide 9: The WLAN Landscape….
802.11a: WLAN in the 5GHz band using OFDM
802.11b: WLAN in the 2.4GHz band using CCK
802.11e: Enhanced QoS
802.11f: Inter-access point protocol
802.11g: WLAN in the 2.4GHz band using OFDM
802.11h: Modifications to 802.11a for Europe
802.11i: Enhanced security (beyond WEP)

## Slide 10: 802.11b/g/a Family of Wireless LANs
802.11b, “g”, and “a” are all part of the same wireless LAN family
  All share a common Media Access Controller (MAC), based on Ethernet
  The three standards differ in the Physical (PHY) layer characteristics
    Modulation techniques, etc.
Other “802.11x” standards refer to MAC enhancements:
  11e: Quality of Service (applies to b/g/a)
  11i: Enhanced security (TKIP/AES) (applies to b/g/a)
  11f (not MAC, more AP Software): Roaming (IAPP) (applies to b/g/a)
  11h: European compatibility for 5GHz (DFS/TPC)

## Slide 11: Wireless WAN
Definition of a WWAN:
  A computer network that spans a relatively large geographical area. Typically, a WAN consists of two or more local-area networks (LANs).
  Computers connected to a wide-area network are often connected through public networks, such as the telephone system. They can also be connected through leased lines or satellites. The largest WAN in existence is the Internet.
  The largest wireless WAN is the mobile telephone system

## Slide 12: What about BWA?
Broadband Wireless Access
  Fixed wireless refers to wireless devices or systems that are situated in fixed locations, such as an office or home, as opposed to devices that are mobile, such as cell phones and PDAs. Fixed wireless devices normally derive their electrical power from utility mains, as opposed to portable wireless devices that normally derive their power from batteries.
  The point-to-point signal transmissions occur through the air over a terrestrial microwave platform rather than through copper or fiber cables; therefore, fixed wireless does not require satellite feeds or local phone service. The advantages of fixed wireless include the ability to connect with users in remote areas without the need for laying new cables and the capacity for broad bandwidth that is not impeded by fiber or cable capacities.

## Slide 13: Broadband Wireless Access (BWA)
Replaces the “last mile” of copper or fiber with wireless
Can use LMDS, MMDS, or other spectrum
Generally fixed terminals
802.16: Air interface for 10-60GHz licensed
  802.16a: 2-11GHz unlicensed
802.16.2: Coexistence for same-band protocols
MBWA: Mobile broadband wireless access study group

## Slide 14: Coexistence: The unlicensed band problem
Many standards have been developed for unlicensed bands:
  2.4GHz: 802.11FH, 802.11DS, 802.11b, Bluetooth, HomeRF, 802.15.3, 802.15.4
  5GHz: 802.16a, 802.11a
Devices sharing the same band will cause degradation
  How much is acceptable ?

## Slide 15: 5. Interference – An Issue in All Unlicensed Bands
900 MHz (US) – cordless phones, some WAN, proprietary LAN, industrial heating
2.4 GHz – cordless phones, Bluetooth, 802.11b (Wi-Fi), HomeRF, microwave ovens
5 GHz – cordless phones, mobile satellite, 802.11a, HiperLAN1/2, HiperPAN, 802.15.3 (proposed), microwave ovens, fixed wireless, radar
902-928MHz
2.4-2.483GHz
5.15-5.35GHz
5.725-5.85GHz
Other ISM
24GHz
60GHz
Multiple standards will exist in all bands
Unlicensed band allocations

## Slide 16: Bluetooth – Illustrative WPAN
Frequency hopper at 1600 hops/sec using 1 MHz wide hops
Typical use <10 meters; data rate = 1 Mbps (~ 728 Kbps)
Master – Slave MAC protocol
Provisions for synchronous voice links (SCO)
Expected to achieve ~ 800 MM units / year by 2004
Power
Low Channel Mid Channel High Channel
2.4 GHz 2.4835 GHz
1 MHz Wide

## Slide 17: IEEE 802.11b – Illustrative WLAN
Direct sequence spread spectrum using ~20 MHz channels
Range <150m free space; data rate = 11Mbps (~ 5-7Mbps)
Ethernet like MAC layer – CSMA/CA
Expected to achieve ~ 30-40 MM units / year by 2004; 80-90 MM installed base
Power
Low Channel Mid Channel High Channel
2.4 GHz 2.4835 GHz
~20 MHz Wide

## Slide 18: Interference is Highly Likely
Bluetooth transmission in 802.11b passband destroys 802.11b signal
Likelihood of collision is 55% for 1500 byte packet
802.11b CSMA/CA back-off algorithms exacerbate problem
Power
Low Channel Mid Channel High Channel
2.4 GHz 2.4835 GHz

## Slide 19: Interference Zones
Graceful degradation (0.5-2 m)
No interference (>2 m)
Significant degradation (<0.5 m)
WLAN (Wi-Fi) and Bluetooth
For separation >0.5 m:
  Throughput improves until 100% @ 2 m
  Voice quality suffers w/o AFH inside 2 m
For separation <0.5 m:
  Significantly reduced throughput
  Voice quality can be poor
  Non linear effects may occur
    Front end compression (blocking)
    Reciprocal mixing (intermods)

## Slide 20: Adaptive FH when collocated
Collocated Adaptive hopping
Link budget
Class 3
Class 1
Transmitted power
0dBm
+20dBm
Path loss[1]
34dB (0.5 m)
46dB (2 m)
Adjacent channel loss
(per 802.11 specification)
35dB
35dB
Power at detector
-69dBm
-61dBm
802.11b detection level
-76dBm
-76dBm
Detectable signal above threshold
7dB
15dB
[1] Assuming the path loss is free space at these short distances: Lp=40+20Log10(d), with d in meters.
AFH does not solve the coexistence problem when Bluetooth and Wi-Fi are collocated
Out of Band Link budget

## Slide 21: IEEE 802.15.2: Coexistence SG
Working on “Recommended Practice” document for Bluetooth-802.11b
Evaluated two types of techniques:
  Collaborative (collocated systems can communicate)
    Manual/Driver/MAC switching
  Non-collaborative (no direct communication; e.g. AFH)
Draft document available from IEEE
Solutions in the market early 2002
Bluetooth SIG also has Coexistence WG
  Chaired by Dr. Tod Sizer of Lucent
  Evaluating a number of techniques and interferers

## Slide 22: Mixing the alphabet soup
In addition to the coexistence problem, there is the migration problem
  Moving everybody to 5GHz doesn’t solve the problem
  Backward compatibility is the problem – hence the need for dual band support

## Slide 23
<number>
Proprietary and Confidential
www.mobilian.com
Notes: <number>
<footer>
<header>
<date/time>
Separate True Connectivity – need device to recognize and connect wireless opportunities; pod printing
Differences between networking types PAN and LAN and impacts on radio types
  Cost, power, range, function (data, voice)
  Multiple standards and need for multiple radio types (leading to standards fragmentation)

## Slide 24: Why WLAN – GPRS/3G interworking?
Requirements:
  needs for “global” roaming and mobility
  needs for high capacity - especially at hot spots
Market:
  Users of PC-type terminals as a part of the 3G operator subscriber base
  3G packet service expansion with small investment costs
  New services and applications
  Increased overall customer value  Increased revenue stream
Notes: With WLANs, cellular operators may relax their plans for 3G deployment, if license agreements allow them to do so.
The requirements presented in the following slides have been defined as of a long-term goal, earlier releases of system solutions may implement limited functionality, and I will come back to that.
By the way, 3G also includes GPRS and Edge in this presentation.

## Slide 25: Emerging trends
For 802.11a: higher speeds (> 100Mb/s)
Better QoS (802.11e)
Better security (802.11i)
Global harmonization (802.11h)
Faster speeds in 2.4GHz (802.11g)
Smart antenna technology
Ultrawide band for short range

## Slide 26: What about Ultra Wide Band (UWB)?
No carrier – pulses injected directly into antenna
Spectral characteristics governed by pulse shape and antenna
Very broadband (>1GHz)
Potentially high data rates (>100Mb/s)
Regulatory bodies are skeptical because of the potential for interference

## Slide 27: Radio Spectrum: A precious resource
Governments sell it
Allocation is now a huge international issue
  WRC 2003
Licensed spectrum predominates
  But purchasing it is risky
    Case in point: 3G!! 
  Always a fight between commercial, civil, military
Unlicensed is attractive to commercial
  Small barrier to entry into market
  Poses large interference problem
So nobody wants to pay for it, but everybody wants the reliability offered by clear spectrum!

## Slide 28: How do you share spectrum?
Power
Frequency
Time
Code
Space
The goal? To make every transmission from A to B reliable

## Slide 29: We have made some advances….
UWB?
  Maybe it’s not really an advance – it’s Marconi’s spark gap generator!
  Radical change in regulatory policies required
OFDM
  Currently the favorite for emerging WLAN/WWAN systems
  Works well with long delay spread
  Combined with QAM, gets high data rates with good spectral efficiency
Shannon always gets in the way….
Moore’s Law doesn’t apply to spectrum!!

## Slide 30: The Highly Adaptive Radio (HAR)
Combines
  Multiple standards (WPAN/WLAN/WWAN)
  Power control (closed loop)
  Smart antennas (SDMA)
  Coding (FEC + CDMA)
  Frequency adaptation (FDMA + DFS)
  Time coordination (TDMA)

## Slide 31: HAR in a current environment
HAR optimizes:
  Cost of connection
  Data rate
  Error rate
By controlling:
  > Protocol (if multiple available)
  Power levels
  Antenna beamforming
  Frequency
  Coding
  Timing
Highly Adaptive Radio
GPRS/EDGE
HDR/1xRTT
3G
802.11b/g
802.11a
HiperLAN2
Bluetooth
WPAN
WLAN
WWAN
OS
Support
( Policy rules,
Load Indicators,
Wireless State Indicators,
Application Indicators,
QoS Indicators,
Usage Profiles,
User Profiles)
Intermediate multiplex driver
Networking / Connectivity Stacks
(TCP/IP / BT)
Applications
Detect
Select
Connect
WWAN Driver
WWAN Driver
WPAN Driver

## Slide 32: Technologies needed for HAR
Software defined radio
  Adapts protocol, modulation, and packets
Smart antennas – cheap
Research in optimization of link quality management
  Optimize data rate and quality of service (delay and/or latency) under the constraints of:
    Packet size
    Coding
    Modulation
    Eb/N0
    Antenna beamwidth

## Slide 33: Example
Device scans environment (DETECT phase)
  Could be WPAN, WLAN, WWAN
Makes decision about wireless system to use based on policy (SELECT phase)
  One policy: always use highest speed untariffed
  Another: Prefer WLAN, then WPAN, then WWAN
Use all tools available to establish robust link (CONNECT phase)
  Use smart antenna to form beam to tower/AP
  Use minimum power to maintain BER/FER/QoS
  Change data rate/FEC to maintain BER/FER/QoS
  Adaptive coding (if possible)
  Vary packet size to suit interference/QoS needs
  Best available channel selection (AFH/DFS/spectral shaping)

## Slide 34: The multi-standard/multi band radio
So called “universal radio”
  DSP allows baseband functions to be performed flexibility
  Doesn’t and can’t replace RF circuitry
  May only be able to do one at a time
Today, these are more likely to be implemented as traditional building blocks on chip
Over time, there will be more DSP based approaches

## Slide 35: The Trend? Multi-standard Radio
802.11b-Bluetooth
  Now a reality
  Integrated approach yields best performance & price
802.11b/a/g – (the whole “bag”)
  Forward backward compatibility
WPAN-WLAN-WWAN
  Works “anytime, anywhere”
Software defined in the future
  Reconfigurable for multiple standards
  Not optimal price-power-performance today
WWAN
(GPRS, UMTS)
WLAN
(802.11b/a/g)
WPAN
(Bluetooth)

## Slide 36: A case study: the WPAN/WLAN combo radio
Combines 802.11b and Bluetooth
Manages interference using
  signal processing
    Both analog and digital
  time scheduling
  allows truly simultaneous operation
    Virtually no loss in performance
Integrated solution drives down cost

## Slide 37: The “True” 11b-Bluetooth combo solution: TrueRadio
Integration
  Decreases overall component count by 33% over current Wi-Fi only designs, and 50% over Wi-Fi and BT
  2-Chip solution
    Single chip contains both radios and the other chip contains both basebands and MACs
True Simultaneous Operation
  Allows for simultaneous operation of BT and Wi-Fi with virtually no degradation to performance, for the best user experience
True simultaneous operation –
both ACL and SCO:
Coexistence without Compromise™

## Slide 38: Conclusion
Wireless combines applications for portable as well as mobile markets
Users will demand increased mobility and performance
Multi-standard radio will allow this heterogeneous mix to be cost effective
Software will be needed to allow these multi-standard radios to roam across systems
Multi-standard will show a trend toward increasing DSP usage in the baseband/MAC